## Slide 1: Thor v8
ALU1
ALU2
Load
AGU
Load
AGU
Store
AGU
FPU1
FPU2
FCU
Reg File
32
Reg File
32
Reg File
32
Reg File
32
Reg File
16
Reg File
16
Reg File
16
Reg File
8
Register files are clustered with execution units
Architectural Registers:
8, 8-bit condition code registers
8, 64-bit code address registers
16, 64-bit address registers
32, 64 to 256-bit data registers
8, segment registers
Physical Registers = Architectural Registers x2
ROB

## Slide 2: FT64 v8 Register File
32 Data Regs
ALU
16 Data Address
Regs
AGU
8 Code Address Regs
Branch
8 Segment Regs
8 Condition
Code Regs
32 Data Regs
FPU
Register files are associated with specific functional units.
There are multiple ALUs, AGUs and FPUs.
There are twice as many physical registers as architectural registers for register renaming.